Gosford Passing Loops Monitoring Data

| Licensee: | Downer Edi Works Pty Ltd | Address: | 15 Watt St, Gosford | EPL No. | 20269 |
| --- | --- | --- | --- | --- | --- |
| Sampled: | Throughout February | Obtained: | Throughout February | Published: | February 2015 |

|  | Noise Monitoring Results |
| --- | --- |
| Location | Date | Time | Measured (LAeq 15 min) | Predicted noise level | Comments |
| Cnr Campbell and Glennie Street | 07/02/2015 | 2350 | 54.6 | 57.3 | Measurement dominated by local clipping of rail and the lighting tower. Local Traffic on Pacific Highway. |
| 77 Showground Road | 08/02/2015 | 0930 | 57.5 | 61.6 | Measurement dominated by local traffic and a freight train and its horn. During the recording period there was also a lawn mower being used. |
| 31 Dwyer Street | 08/02/2015 | 0954 | 53.6 | 64.7 | Measurement dominated by local traffic on Showground Road and go-carts. |
| 28 Akora Road | 08/02/2015 | 1021 | 64.3 | 62.3 | Measurement dominated by local traffic on Pacific Highway, birds and a freight train passing. It is noted that the measured is within 2dbA of the predicted and the dominant noise source is not related to the project activities but rather local traffic and residential activities. |
| 77 Showground Road | 08/02/2015 | 2255 | 55.9 | 61.6 | Measurement dominated by local traffic, crickets and dogs in the distance. |
| 77 Showground Road | 09/02/2015 | 2310 | 52.3 | 61.6 | Measurement dominated by local traffic on Showground Road, people at the oval on Showground Road, bats, possums crickets and dogs barking. |
| 8 Akora Road | 09/02/2015 | 2340 | 51.1 | 62.3 | Measurement dominated by local traffic on Pacific Highway, people at the oval on Showground Road, bats, possums and crickets. Council weed spraying and sweeper. |
| 77 Showground Road | 09/02/2015 | 0040 | 52.0 | 61.6 | Measurement dominated by local traffic on Pacific Highway, bats, possums and crickets. Road works being conducted on Pacific Highway near McDonalds. Minor construction works could be heard. |
| 77 Showground Road | 10/02/2015 | 0120 | 52.7 | 61.6 | Measurement dominated by local traffic on Showground Road, bats, possums, crickets and dogs barking. |
| 8 Akora Road | 10/02/2015 | 0155 | 50.1 | 62.3 | Measurement dominated by local traffic on Pacific Highway, people at the oval on Showground Road, bats, possums and crickets. |
| 77 Showground Road | 16/02/2015 | 1120 | 54.9 | 61.6 | Measurement dominated by bats, possums and crickets. As well as passing cars and a freight train. |
| Glennie Street West | 17/02/2015 | 0200 | 70.7 | 70.0 | The exceedence of the predicted is less than 1dbA with the measurement dominated by local traffic on Mann Street and Showground Road and bats rather than project construction noise. Site noise was dominant when the grinder was passing within approximately 100m either side of the location, although the grinder pass lasted for approximately one minute of the 15 minute duration. |
| 77 Showground Road | 21/02/2015 | 0415 | 59.7 | 51.2 | Measurement dominated by bats, frogs and crickets. As well as passing cars and buses Showground Road (road was wet). No audible project construction noise. |
| 77 Showground Road | 21/02/2015 | 1015 | 56.1 | 51.2 | Measurement dominated by cars and buses, as well as people talking in the distance. No audible project construction noise |

NOTES

Monitoring results showed that actual noise impacts in most instances were below predicted levels during the February 2015 works. There were four exceedances during the reporting period. In all instances the main noise was dominated by non-construction activities such as the fauna, local traffic and people of the community. On the 17 February 2015, there was an exceedance from which was contributed to by the passing of the track grinder as well as outside influences such as local traffic. The grinder was a small portion of the overall monitoring period and overall noise exceedence was less that 1dbA of the predicted. It is likely that the exceedence is a combination of the passing grinder and local noise sources. It is noted the monitoring location was side of track and is closer than any residences and is not obstructed by fences / elevations as residential receivers are in this location. Therefore is it considered likely that the actual noise at the residential receiver wold be compliant with the prediction. Affected sensitive receivers were notified of the upcoming works via letter box drops and door knocks as per the community liaison plan.

Dust Deposition Results

Air concentration limits are specified in EPL Condition L2.4.  Table 2 specifies the Air Concentration Limits for the Project.

Table 2 Air Concentration Limits

| Pollutant | Units of Measure | 100 percentile concentration limit | Reference Conditions | Oxygen correction | Averaging period |
| --- | --- | --- | --- | --- | --- |
| Insoluble solids | Grams per square metre per month | 4 | Maximum total insoluble solids |  | Month |

Details on the location of the three Dust Deposition Gauges are provided in Table 3 and in Figure 1. The monitoring locations are consistent with EPL Condition P1.1.

Table 3 Monitoring Locations

| EPA Identification no. | Type of Monitoring Point | Location Description |
| --- | --- | --- |
| 2 | Dust deposition gauge (reference gauge) | 73A Showground Road, Narara |
| 3 | Dust deposition gauge | 520 Pacific Highway, Wyoming (near crusher site) |
| 4 | Dust deposition gauge | 4 Renwick Street Wyoming (crusher site) |

Table 4 Monitoring Results

| Monitoring Point | Date | Units of Measure | Insoluble solids | 100 percentile concentration limit |
| --- | --- | --- | --- | --- |
| February 2015 |
| EPA 2 | 15/01/15 – 17/02/15 | Grams per square metre per month | 0.7 | 4 |
| EPA 3 | 15/01/15 – 17/02/15 | Grams per square metre per month | 0.4 | 4 |
| EPA 4 | 15/01/15 – 17/02/15 | Grams per square metre per month | 1.2 | 4 |

Surface Water Discharge Monitoring

Licence condition L2.1 states that for each monitoring discharge point or utilisation area specified in the table below, the concentration of a pollutant discharged at that point, or applied to that area, must not exceed the concentration limits specified for that pollutant in the table Licence condition L2.5 details water concentration limits. These limits are detailed below in Table 4. The monitoring data results can be found in Table 5.

Table 4- Water concentration limits

| Pollutant | Units of Measure | 100 percentile concentration limit |
| --- | --- | --- |
| Oil and grease | Visible | Visible |
| pH | pH | 6.5 – 8.5 |
| Total Suspended Solids | Milligrams per litre (mg/L) | 50 |

Surface water discharge monitoring results for February 2015

No Surface Water Discharge Points were used during the February 2015 reporting period.