Gosford Passing Loops Monitoring Data

| Licensee: | Downer Edi Works Pty Ltd | Address: | 15 Watt St, Gosford | EPL No. | 20269 |
| --- | --- | --- | --- | --- | --- |
| Sampled: | Throughout September | Obtained: | Throughout September | Published: | 08/10/2014 |

|  | Noise Monitoring Results |
| --- | --- |
| Location | Date | Time | Measured (LAeq 15 min) | Predicted noise level | Comments |
| 77 Showground Road | 01/09/14 | 2321 | 54.1 | 58.0 | Delivery of rail. Site works were inaudible with the measurement dominated by traffic and train and their horns. |
| 24 Campbell Street | 01/09/14 | 2349 | 47.4 | 69.3 | Use of vac truck for non-destructive digging and 5t excavator. |
| 31 Dwyer Street | 02/09/14 | 0010 | 41.4 | 69.3 | Use of vac truck for non-destructive digging and 8t excavator. Measurement dominated by traffic. |
| 77 Showground Road | 02/09/14 | 0034 | 49.5 | 58.0 | Delivery of rail. Site works were inaudible with the measurement dominated by traffic and train horns. |
| 24 Campbell Street | 02/09/14 | 0057 | 49.3 | 69.3 | Use of vac truck for non-destructive digging and 8t excavator. |
| 77 Showground Road | 02/09/14 | 2250 | 55.5 | 58.0 | Delivery of rail. Site works were inaudible with the measurement dominated by traffic and train and their horns. |
| 24 Campbell Street | 02/09/14 | 2315 | 59.5 | 69.3 | Use of vac truck for non-destructive digging and 5t excavator. |
| 30 Akora Road | 02/09/14 | 2340 | 58.0 | 65.0 | Overhead removal, which included hand tools and a crane. Measurement dominated by traffic and train and their horns. |
| 10 Akora Road | 03/09/14 | 0000 | 65.2 | 65.0 | Overhead removal, which included hand tools and a crane. Measurement dominated by train and train horn. |
| 24 Campbell Street | 03/09/14 | 0027 | 58.7 | 69.3 | Use of vac truck for non-destructive digging and 5t excavator. |
| 30 Akora Road | 03/09/14 | 0050 | 47.7 | 65.0 | Overhead removal, which included hand tools and a crane. |
| 31 Dwyer Street | 06/09/14 | 0823 | 53.0 | 51.4 | ULX works with an 8t excavator operating 49dB. Measurement dominated by vehicles passing on Showground RD. |
| 24 Campbell Street | 06/09/14 | 0848 | 53.2 | 69.3 | Switch yard construction using a 20t and 12t excavator, 1 dump truck, and a vac truck. |
| 10 Akora Road | 06/09/14 | 0912 | 51.4 | 55.9 | Overhead footing construction involving excavator. Measurement dominated by chainsaws and vehicles. |
| 77 Showground Road | 06/09/14 | 1109 | 63.0 | 54.6 | Overhead footings with 12t excavator operating. Measurement dominated by constant vehicles passing. |
| 77 Showground Road | 06/09/14 | 1423 | 63.5 | 54.6 | Overhead footings with 12t excavator operating. Measurement dominated by constant vehicles passing. |
| 31 Dwyer Street | 06/09/14 | 1448 | 57.5 | 67.1 | Overhead wiring works and a ULX construction. |
| 24 Campbell Street | 06/09/14 | 1520 | 59.5 | 69.3 | Switch yard works using a 20t and 12t excavator and 1 dump truck. Measurement dominated by vehicles passing. |
| 10 Akora Road | 06/09/14 | 1544 | 49.3 | 55.9 | Overhead footings with 8t excavator operating. Measurement dominated by vehicles passing. |
| 31 Dwyer Street | 07/09/14 | 0804 | 50.7 | 67.1 | Overhead wiring works and a local trench. Works being conducted with multiple hi-rails and an 8t excavator. Measurement dominated by vehicles passing on Showground Road. |
| 24 Campbell Street | 07/09/14 | 0826 | 57.6 | 69.3 | Switch yard construction using a 20t and 12t excavator, 1 moxy, and a vac truck. |
| 10 Akora Road | 07/09/14 | 0922 | 47.7 | 55.9 | Overhead footings with 8t excavator operating and a small generator. |
| 77 Showground Road | 07/09/14 | 1005 | 62.8 | 54.6 | Overhead footings with 8t excavator operating and two EWP’s. Measurement dominated by vehicles passing on Showground Road. |
| 31 Dwyer Street | 08/09/14 | 0145 | 43.4 | 49.9 | OHW works involving a Crane and lighting tower. |

NOTES

Monitoring results showed that actual noise impacts were below predicted levels. Four exccedances were recorded due to the high level of non-construction related noise at receiver (frequent vehicle pass). Observations during the measurement showed construction impacts were inaudible. Affected sensitive receivers were notified of the upcoming works via letter box drops

Dust Deposition Results

Air concentration limits are specified in EPL Condition L2.4.  Table 2 specifies the Air Concentration Limits for the Project.

Table 2 Air Concentration Limits

| Pollutant | Units of Measure | 100 percentile concentration limit | Reference Conditions | Oxygen correction | Averaging period |
| --- | --- | --- | --- | --- | --- |
| Insoluble solids | Grams per square metre per month | 4 | Maximum total insoluble solids |  | Month |

Details on the location of the three Dust Deposition Gauges are provided in Table 3 and in Figure 1. The monitoring locations are consistent with EPL Condition P1.1.

Table 3 Monitoring Locations

| EPA Identification no. | Type of Monitoring Point | Location Description |
| --- | --- | --- |
| 2 | Dust deposition gauge (reference gauge) | 73A Showground Road, Narara |
| 3 | Dust deposition gauge | 520 Pacific Highway, Wyoming (near crusher site) |
| 4 | Dust deposition gauge | 4 Renwick Street Wyoming (crusher site) |

Table 4 Monitoring Results

| Monitoring Point | Date | Units of Measure | Insoluble solids | 100 percentile concentration limit |
| --- | --- | --- | --- | --- |
| September 2014 |
| EPA 2 | 15/08/14 – 15/09/14 | Grams per square metre per month | 1.5 | 4 |
| EPA 3 | 15/08/14 – 15/09/14 | Grams per square metre per month | 0.7 | 4 |
| EPA 4 | 15/08/14 – 15/09/14 | Grams per square metre per month | 0.7 | 4 |

Surface Water Discharge Monitoring

Licence condition L2.1 states that for each monitoring discharge point or utilisation area specified in the table below, the concentration of a pollutant discharged at that point, or applied to that area, must not exceed the concentration limits specified for that pollutant in the table Licence condition L2.5 details water concentration limits. These limits are detailed below in Table 4. The monitoring data results can be found in Table 5.

Table 4- Water concentration limits

| Pollutant | Units of Measure | 100 percentile concentration limit |
| --- | --- | --- |
| Oil and grease | Visible | Visible |
| pH | pH | 6.5 – 8.5 |
| Total Suspended Solids | Milligrams per litre (mg/L) | 50 |

Table 5- Surface water discharge monitoring results for September 2014

| EPA Monitoring Point | Location | Total Suspended Solids (mg/L) | Turbidity (NTU) | pH | Oil and Grease | Date of Release |
| --- | --- | --- | --- | --- | --- | --- |
| 1 | Brady's Gully | 12.2 | 27.7 | 7.2 | Not visible | 2/09/2014 |
| 5 | Lindsey St (E4) | 15.6 | 18.8 | 7 | Not visible | 3/09/2014 |
| 8 | Wyoming Creek | 43.0 | 51.8 | 6.8 | Not visible | 3/09/2014 |
| 1 | Brady's Gully | 13.0 | 29.6 | 8.4 | Not visible | 4/09/2014 |
| 5 | Lindsey St (E4) | 12.9 | 15.6 | 7.8 | Not visible | 4/09/2014 |
| 5 | Lindsey St (E4) | 7.4 | 8.91 | 7.08 | Not visible | 4/09/2014 |
| 1 | Brady's Gully | 5.7 | 12.9 | 7.4 | Not visible | 5/09/2014 |
| 1 | Brady's Gully | 6.6 | 15.1 | 7.2 | Not visible | 6/09/2014 |
| 5 | Lindsey St (E4) | 33.0 | 39.8 | 7.4 | Not visible | 6/09/2014 |
| 1 | Brady's Gully | 15.0 | 34 | 7.5 | Not visible | 7/09/2014 |
| 1 | Brady's Gully | 11.4 | 25.9 | 8 | Not visible | 7/09/2014 |
| 1 | Brady's Gully | 15.0 | 34.2 | 6.9 | Not visible | 8/09/2014 |
| 1 | Brady's Gully | 15.4 | 35 | 6.8 | Not visible | 9/09/2014 |
| 1 | Brady's Gully | 9.2 | 21 | 6.8 | Not visible | 10/09/2014 |
| 8 | Wyoming Creek | 17.4 | 21 | 6.8 | Not visible | 10/09/2014 |
| 1 | Brady's Gully | 24.3 | 29.3 | 7.2 | Not visible | 10/09/2014 |
| 1 | Brady's Gully | 14.2 | 32.3 | 6.8 | Not visible | 10/09/2014 |
| 8 | Wyoming Creek | 13.6 | 16.4 | 6.8 | Not visible | 11/09/2014 |
| 1 | Brady's Gully | 9.5 | 21.7 | 7.3 | Not visible | 15/09/2014 |
| 1 | Brady's Gully | 10.0 | 22.8 | 6.8 | Not visible | 16/09/2014 |
| 1 | Brady's Gully | 12.3 | 28 | 7.8 | Not visible | 17/09/2014 |
| 1 | Brady's Gully | 12.3 | 28 | 6.9 | Not visible | 18/09/2014 |
| 1 | Brady's Gully | 12.3 | 27.9 | 6.9 | Not visible | 19/09/2014 |
| 1 | Brady's Gully | 13.3 | 30.2 | 6.9 | Not visible | 20/09/2014 |
| 1 | Brady's Gully | 9.9 | 22.4 | 7.1 | Not visible | 22/09/2014 |
| 1 | Brady's Gully | 10.1 | 22.9 | 6.7 | Not visible | 23/09/2014 |
| 1 | Brady's Gully | 10.6 | 24.2 | 7.2 | Not visible | 24/09/2014 |